## Slide 1: CSC 221 Computer Organization and Assembly Language
Lecture 05: Memory Access

## Slide 2: Lecture 4: Review
The programming model of the 8086 through 80286 contain 8- and 16-bit registers.
The programming model of the 80386 and above contains 8-, 16-, and 32-bit extended registers as well as two additional 16-bit segment registers: FS and GS.

## Slide 3: Lecture 4: Review
The 64-bit registers in a Pentium 4 with 64-bit extensions are RAX, RBX, RCX, RDX, RSP, RBP, RDI, RSI, and R8 through R15.
In addition, the microprocessor contains an instruction pointer (IP/EIP/RIP) and flag register (FLAGS, EFLAGS, or RFLAGS).
(cont.)

## Slide 4: Lecture Outline
Memory Access:
  Real Mode memory-addressing techniques.
  Protected Mode memory-addressing techniques.
Memory Access:
  64-bit Flat Memory model.
Program-invisible registers in the 80286~Core2 microprocessors.

## Slide 5: REAL MODE MEMORY ADDRESSING
The only mode available on the 8086-8088.
20 bit address bus  1 MB, 16 bit data bus, 16 bit registers
80286 and above operate in either the real or protected mode.
Real mode operation allows addressing of only the first 1M byte of memory space—even in Pentium 4 or Core2 microprocessor.
  the first 1M byte of memory is called the real memory, conventional memory, or DOS memory system

## Slide 6: Segments and Offsets
All real mode memory addresses must consist of a segment address plus an offset address.
  segment address defines the beginning address of any 64K-byte memory segment
  offset address selects any location within the 64K byte memory segment
Figure in Next Slide: shows how the segment plus offset addressing scheme selects a memory location.

## Slide 7: Figure: The real mode memory-addressing scheme, using a segment address plus an offset.
  this shows a memory segment beginning at 10000H, ending at location IFFFFH
    64K bytes in length
  also shows how an offset address, called a displacement, of F000H selects location 1F000H in the memory
Segments and Offsets

## Slide 8: Figure: The real mode memory-addressing scheme, using a segment address plus an offset.
Segments and Offsets
16-bit each
Appended 4 bits (0H)
Segment Start Address
in Segment Register
0
Then the Effective memory Address (EA) =
20-bit segment start address +
16-bit offset address

## Slide 9
Effective Address Calculations
EA = segment register (SR) x 10H + offset
(a) SR: 1000H
10000 + 0023 = 10023H
(b) SR: AAF0H
AAF00 + 0134 = AB034H
(c) SR: 1200H
12000 + FFF0 = 21FF0H

## Slide 10: Segments and Offsets
Once the beginning/starting address is known, the ending address is found by adding FFFFH.
  because a real mode segment of memory is 64K in length
The offset address is always added to the segment starting address to locate the data.
Segment and offset address is sometimes written as 1000:2000.
  a segment address of 1000H; an offset of 2000H

## Slide 11: Default Segment and Offset Registers
The microprocessor has rules that apply to segments whenever memory is addressed.
  these define the segment and offset register combination
The code segment register defines the start of the code segment.
The instruction pointer locates the next instruction within the code segment.

## Slide 12: Default Segment and Offset Registers
Another of the default combinations is the stack.
  stack data are referenced through the stack segment at the memory location addressed by either the stack pointer (SP/ESP) or the base pointer (BP/EBP)
Figure in Next Slide: shows a system that contains four memory segments.
  a memory segment can touch or overlap if 64K bytes of memory are not required for a segment

## Slide 13: Figure: A memory system showing the placement of four memory segments.
  think of segments as Windows that can be moved over any area of memory to access data or code
  a program can have more than four or six segments,
    but only access four or six segments at a time
Default Segment and Offset Registers
00000
Stack
Code
Data
Extra
0FFFF
10000
1FFFF
20000
2FFFF
30000
33FFF
34000
43FFF
44000
48FFF
49000
58FFF
59000
FFFFF
Memory
1 0 0 0
DS
2 0 0 0
CS
3 4 0 0
SS
4 9 0 0
ES

## Slide 14: Figure: An application program containing a code, data, and stack segment loaded into a DOS system memory.
Default Segment and Offset Registers
Code should be limited to only this portion of the code segment, to avoid effects of segment overlap.

## Slide 15: Default Segment and Offset Registers
Default segment numbers in:
  CS for program (code)
  SS for stack
  DS for data
  ES for string (destination) data
Default offset addresses that go with them:
Segment | Offset (16-bit) 8080, 8086, 80286 | Offset (32-bit) 80386 and above | Purpose
CS | IP | EIP | Program
SS | SP, BP | ESP, EBP | Stack
DS | BX, DI, SI, 8-bit or 16-bit # | EBX, EDI, ESI, EAX ECX, EDX, 8-bit or 32-bit # | Data
ES | DI, with string instructions | EDI, with string instructions | String destination
Convention Example: EA = CS:[IP]
Segment Start
in Segment register
Offset: Literal
or in a CPU register

## Slide 16: TPA
The Transient Program Area (TPA) holds the DOS (disk operating system) operating system; other programs that control the computer system.
TPA is the first available area of memory above drivers and other TPA programs
Area is indicated by a free-pointer maintained by DOS
program loading is handled automatically by the program loader within DOS

## Slide 17: Real Mode Addressing Scheme Allows Relocation
Segment plus offset addressing allows DOS programs to be relocated in memory.
A relocatable program is one that can be placed into any area of memory and executed without change.
Relocatable data are data that can be placed in any area of memory and used without any change to the program.

## Slide 18: Real Mode Addressing Scheme Allows Relocation
Because memory is addressed within a segment by an offset address, the memory segment can be moved to any place in the memory system without changing any of the offset addresses.
Only the contents of the segment register must be changed to address the program in the new area of memory.
Windows programs are written assuming that the first 2G of memory are available for code and data.

## Slide 19: Real Mode : Pros and Cons
Advantages:
Allows easy and efficient relocation of code and data
To relocate code or data, only the number in the relevant segment register needs to be changed
Consequences:
A program can be located anywhere in memory without making any changes to it (addresses are not absolute, but offsets relative to start of segments)
Program writer needs not worry about actual memory structure (map) of the computer used to execute it
Disadvantages:
Complex hardware and for address generation
Address computation delay for every memory access
Software limitation: Program size limited by segment size (64KB with the 8086)

## Slide 20: Limitations of the Real Mode Segmentation Scheme
Segment size is fixed at and limited to 64 KB
Segment can not begin at an arbitrary memory address…
With 20-bit memory addressing, can only begin at addresses starting with 0H, i.e. at 16 byte intervals
 Principle is difficult to apply with 80286 and above, with segment registers remaining at 16-bits!
80286 and above use 24, 32 bit addresses but still 16-bit segment registers
No protection mechanisms: Programs can overwrite operating system code segments and corrupt them!
 Use memory segmentation in the protected mode
Append: 00H 0000H

## Slide 21: PROTECTED MODE MEMORY ADDRESSING
Operating systems operate in a 16- or 32-bit environment.
DOS uses a 16-bit environment.
Most Windows applications use a 32-bit environment called WIN32.
MSDOS/PCDOS & Windows 3.1 operating systems require 16-bit instruction mode.
Instruction mode is accessible only in a protected mode system such as Windows Vista.

## Slide 22: PROTECTED MODE MEMORY ADDRESSING: 80286 and above
Allows access to data and programs located within and above the first 1M byte of memory.
Protected mode is where Windows operates.
In place of a segment address, the segment register contains a selector that selects a descriptor from a descriptor table.
The descriptor describes the memory segment’s location, length, and access rights.
Descriptors are placed in descriptor tables in main memory
Protection is provided by restricting access to memory segments through:
- Privilege levels,
- and Access rights

## Slide 23: Selectors and Descriptors
The descriptor is located in the segment register and describes the location, length, and access rights of the segment of memory.
  it selects one of 8192 descriptors from one of two tables of descriptors
In protected mode, this segment number can address any memory location in the system for the code segment.
Indirectly, the register still selects a memory segment, but not directly as in real mode.

## Slide 24: Selectors and Descriptors
Global descriptors contain segment definitions that apply to all programs.
Local descriptors are usually unique to an application.
  a global descriptor might be called a system descriptor, and local descriptor an application descriptor
Figure 2–6 shows the format of a descriptor for the 80286 through the Core2.
  each descriptor is 8 bytes in length
  global and local descriptor tables are a maximum of 64K bytes in length

## Slide 25: Figure: The 80286 through Core2 64-bit descriptors.
Base: 3-byte
Limit: 2-byte (16 bit)
 Seg. Size: 1B-64 KB
Note provision for upward compatibility (286 software run on higher processors)
Base: 4-byte
 32 bit addressing
Limit: 2-1/2-byte (20 bit)
 Size: 1B-1MB
With G (4 K multiplier) bit = 1: 4KB-4GB
Instruction
Mode: 16/32 bits
Segment
Availability

## Slide 26: Descriptors
The base address of the descriptor indicates the starting location of the memory segment.
  the paragraph boundary limitation is removed in protected mode
  segments may begin at any address
The G, or granularity bit allows a segment length of 4K to 4G bytes in steps of 4K bytes.
  32-bit offset address allows segment lengths of 4G bytes
  16-bit offset address allows segment lengths of 64K bytes.

## Slide 27: Descriptors
The G, or granularity bit allows a segment length of 4K to 4G bytes in steps of 4K bytes.
If G=0: no change
If G=1, append limit with FFFH, i.e. segment size is multiplied by 4K
With limit specifying 1 MB segments and G=1 (i.e. 4K multiplier): Max Segment size = 4K x 1 MB = 4 GB
With 16K segments like this, the system can address 16K x 4 GB = 64 TB (not necessarily all will be in physical memory)

## Slide 28: 80386 and above Example
Descriptor has: base = 23000000H
limit = 012FFH
With G = 0
Segment start = 23000000H
Segment end = 23000000H + 012FFH=230012FFH
Segment size = 12FFH+1H = 1300H
(= 19 x 256 bytes)
With G = 1 ( so actual limit = 012FFFFFH) (append limit in descriptor by FFFH)
Segment start = 23000000H
Segment end = 23000000H + 012FFFFFH = 242FFFFFH
Segment size = 12FFFFF+1H = 1300000H = 212 x 1300H
= 4K x 1300H

## Slide 29: Access Rights Byte
The access rights byte controls access to the protected mode segment.
  describes segment function in the system and allows complete control over the segment
  if the segment is a data segment, the direction of growth is specified
If the segment grows beyond its limit, the operating system is interrupted, indicating a general protection fault.
You can specify whether a data segment can be written or is write-protected.

## Slide 30: Figure: The access rights byte for the 80286 through Core2 descriptor.
DPL will be compared with
the request privilege level
(RPL) in the segment register
specifying this segment.
Allow access to the
segment only if RPL has
higher or equal privilege
to the DPL, subject to the
state of C bit if applicable

## Slide 31: Descriptor Table
Descriptors are chosen from the descriptor table by the segment register.
  register contains a 13-bit selector field, a table selector bit, and requested privilege level field
The TI bit selects either the global or the local descriptor table.
Requested Privilege Level (RPL) requests the access privilege level of a memory segment.
  If privilege levels are violated, system normally indicates an application or privilege level violation

## Slide 32: Figure: The contents of a segment register during protected mode operation of the 80286 through Core2 microprocessors.
Segment Register, e.g. DS
Segment number (still in a 16-bit segment register) defines the segment through a selector/descriptor (not directly as in real mode  but more flexibility)
16 bits segment register = 13 bit descriptor selector + 1 bit descriptor table selector + 2-bit requested privilege
Descriptors specify memory segments

## Slide 33: Privilege Levels
Highest
Lowest
Hardware
Privilege
Comparator
DPL
(in descriptor)
RPL
(In Seg Reg)
RPL  DPL
Allow
Access
to segment
00: Highest Privilege
01
10
11: Lowest Privilege

## Slide 34: Discussion
Figure in “Next Slide” in shows how the segment register, containing a selector, chooses a descriptor from the global descriptor table.
The entry in the global descriptor table selects a segment in the memory system.
Descriptor zero is called the null descriptor, must contain all zeros, and may not be used for accessing memory.

## Slide 35
Base
Limit
Processor: 80286
Segment size
= Limit+1
= FF+1
= 100H bytes
Access
Rights byte
H
24-bit Address
Always 0’s for
upward
compatibility
8-byte Segment
Descriptor # 1
MSB
16-bit
Segment
Register
(in main memory)
Protected Mode: Segmentation Example
GDT Base Address
000b
Descriptor # 0
Because each descriptor in
the table is 8 bytes wide,
Selector:000b
is used as an offset from GDT (or LDT) base address to point to the start of the required segment descriptor
(= segment #)
Offset

## Slide 36: Program-Invisible Registers
Global and local descriptor tables are found in the memory system.
To access and specify the table addresses, 80286–Core2 contain program-invisible registers.
  not directly addressed by software
Each segment register contains a program-invisible portion used in the protected mode.
  often called cache memory because cache is any memory that stores information

## Slide 37: Figure: The program-invisible register within the 80286–Core2 microprocessors.

## Slide 38: Discussion
When a new segment number is placed in a segment register, the microprocessor accesses a descriptor table and loads the descriptor into the program-invisible portion of the segment register.
  held there and used to access the memory segment until the segment number is changed
This allows the microprocessor to repeatedly access a memory segment without referring to the descriptor table.
  hence the term cache

## Slide 39: Global Descriptor Table Register
The GDTR (global descriptor table register) and IDTR (interrupt descriptor table register) contain the base address of the descriptor table and its limit.
  when protected mode operation desired, address of the global descriptor table and its limit are loaded into the GDTR
The location of the local descriptor table is selected from the global descriptor table.
  one of the global descriptors is set up to address the local descriptor table

## Slide 40: Local Descriptor Table Register
To access the local descriptor table, the LDTR (local descriptor table register) is loaded with a selector.
  selector accesses global descriptor table, & loads local descriptor table address, limit, & access rights into the cache portion of the LDTR
The TR (task register) holds a selector, which accesses a descriptor that defines a task.
  a task is most often a procedure or application
Allows multitasking systems to switch tasks to another in a simple and orderly fashion.

## Slide 41: Flat Mode Memory
A flat mode memory system is one in which there is no segmentation.
  does not use a segment register to address a location in the memory
First byte address is at 00 0000 0000H; the last location is at FF FFFF FFFFH.
  address is 40-bits
The segment register still selects the privilege level of the software.

## Slide 42: Flat Mode Memory
Real mode system is not available if the processor operates in the 64-bit mode.
Protection and paging are allowed in the 64-bit mode.
The CS register is still used in the protected mode operation in the 64-bit mode.
Most programs today are operated in the IA32 compatible mode.
  current software operates properly, but this will change in a few years as memory becomes larger and most people have 64-bit computers

## Slide 43: Figure The 64-bit flat mode memory model.

## Slide 44: SUMMARY
All real mode memory addresses are a combination of a segment address plus an offset address.
The starting location of a segment is defined by the 16-bit number in the segment register that is appended with a hexadecimal zero at its rightmost end.
The offset address is a 16-bit number added to the 20-bit segment address to form the real mode memory address.
All instructions (code) are accessed by the combination of CS (segment ad-dress) plus IP or EIP (offset address).

## Slide 45: SUMMARY
Data are normally referenced through a combination of the DS (data segment) and either an offset address or the contents of a register that contains the offset address.
The 8086-Core2 use BX, DI, and SI as default offset registers for data if 16-bit registers are selected.
The 80386 and above can use the 32-bit registers EAX, EBX, ECX, EDX, EDI, and ESI as default offset registers for data.
(cont.)

## Slide 46: SUMMARY
The 80286 microprocessor allows a memory segment to start at any of its 16M bytes of memory using a 24-bit base address.
The 80386 and above allow a memory segment to begin at any of its 4G bytes of memory using a 32-bit base address.
This allows an 80286 memory segment limit of 64K bytes, and an 80386 and above memory segment limit of either 1M bytes.
(cont.)

## Slide 47: SUMMARY
The segment register contains three fields of information in the protected mode.
The leftmost 13 bits of the segment register address one of 8192 descriptors from a descriptor table.
The program-invisible registers are used by the 80286 and above to access the descriptor tables.
(cont.)

## Slide 48: SUMMARY
Each segment register contains a cache portion that is used in protected mode to hold the base address, limit, and access rights acquired from a descriptor.
The cache allows the microprocessor to access the memory segment without again referring to the descriptor table until the segment register's contents are changed.
(cont.)

## Slide 49: SUMMARY
The flat mode memory contains 1T byte of memory using a 40-bit address.
In the future, Intel plans to increase the address width to 52 bits to access 4P bytes of memory.
The flat mode is only available in the Pentium 4 and Core2 that have their 64-bit extensions enabled.
(cont.)