## Slide 1: CSC 221 Computer Organization and Assembly Language
Lecture 20:
Conditional and Block Structures

## Slide 2: Lecture 19: Review
I/O Instructions
  StdIn proc lpszBuffer:DWORD,bLen:DWORD
  StdOut proc lpszText:DWORD
  invoke StdOut, addr message1
  invoke StdIn, addr buffer, 100
Conditional Jumps
  Specific flags
  Equality
  Unsigned comparisons
  Signed Comparisons

## Slide 3: Lecture 19: Review
Conditional Jumps
  JB, JC jump to a label if the Carry flag is set
  JE, JZ jump to a label if the Zero flag is set
  JS jumps to a label if the Sign flag is set
  JNE, JNZ jump to a label if the Zero flag is clear
  JECXZ jumps to a label if ECX equals 0
Assembly Examples
(cont.)

## Slide 4: Lecture Outline
Bit Test Instruction
Conditional LOOP Instructions
  LOOPZ and LOOPE
  LOOPNZ and LOOPNE
Block Structures
  Block-Structured IF Statements
  Compound Expressions with AND
  Compound Expressions with OR
  WHILE Loops
  REPEAT Loops

## Slide 5: BT (Bit Test) Instruction
Copies bit n from an operand into the Carry flag
Syntax: BT bitBase, n
  bitBase may be r/m16 or r/m32
  n may be r16, r32, or imm8
Example: jump to label L1 if bit 9 is set in the AX register:
bt AX,9 ; CF = bit 9
jc L1 ; jump if Carry

## Slide 6: Conditional Loop Instructions
LOOPZ and LOOPE
LOOPNZ and LOOPNE

## Slide 7: LOOPZ and LOOPE
Syntax:
  LOOPE destination
  LOOPZ destination
Logic:
  ECX  ECX – 1
  if ECX > 0 and ZF=1, jump to destination
Useful when scanning an array for the first element that does not match a given value.

## Slide 8: LOOPNZ and LOOPNE
LOOPNZ (LOOPNE) is a conditional loop instruction
Syntax:
LOOPNZ destination
LOOPNE destination
Logic:
  ECX  ECX – 1;
  if ECX > 0 and ZF=0, jump to destination
Useful when scanning an array for the first element that matches a given value.

## Slide 9: LOOPNZ Example
.data
array SWORD -3,-6,-1,-10,10,30,40,4
sentinel SWORD 0
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
next:
  test WORD PTR [esi],8000h ; test sign bit
  pushfd ; push flags on stack
  add esi,TYPE array
  popfd ; pop flags from stack
  loopnz next ; continue loop
  jnz quit ; none found
  sub esi,TYPE array ; ESI points to value
quit:
The following code finds the first positive value in an array:

## Slide 10: Drill . . .
.data
array SWORD 50 DUP(?)
sentinel SWORD 0FFFFh
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
L1: cmp WORD PTR [esi],0 ; check for zero
(fill in your code here)
quit:
Locate the first nonzero value in the array. If none is found, let ESI point to the sentinel value:

## Slide 11: . . . (solution)
.data
array SWORD 50 DUP(?)
sentinel SWORD 0FFFFh
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
L1: cmp WORD PTR [esi],0 ; check for zero
  pushfd ; push flags on stack
  add esi,TYPE array
  popfd ; pop flags from stack
  loope L1 ; continue loop
  jz quit ; none found
  sub esi,TYPE array ; ESI points to value
quit:

## Slide 12: Conditional Structures
Block-Structured IF Statements
Compound Expressions with AND
Compound Expressions with OR
WHILE Loops
REPEAT Loops

## Slide 13: Block-Structured IF Statements
Assembly language programmers can easily translate logical statements written in C++/Java into assembly language. For example:
  mov eax,op1
  cmp eax,op2
  jne L1
  mov X,1
  jmp L2
L1: mov X,2
L2:
if( op1 == op2 )
X = 1;
else
X = 2;

## Slide 14: Drill . . .
Implement the following pseudocode in assembly language. All values are unsigned:
  cmp ebx,ecx
  ja next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 15: Drill . . .
Implement the following pseudocode in assembly language. All values are 32-bit signed integers:
  mov eax,var1
  cmp eax,var2
  jle L1
  mov var3,6
  mov var4,7
  jmp L2
L1: mov var3,10
L2:
if( var1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
(There are multiple correct solutions to this problem.)

## Slide 16: Compound Expression with AND (1 of 3)
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped:
if (al > bl) AND (bl > cl)
X = 1;

## Slide 17: Compound Expression with AND (2 of 3)
cmp al,bl ; first expression...
ja L1
jmp next
L1:
cmp bl,cl ; second expression...
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next:
if (al > bl) AND (bl > cl)
X = 1;
This is one possible implementation . . .

## Slide 18: Compound Expression with AND (3 of 3)
cmp al,bl ; first expression...
jbe next ; quit if false
cmp bl,cl ; second expression...
jbe next ; quit if false
mov X,1 ; both are true
next:
if (al > bl) AND (bl > cl)
X = 1;
But the following implementation uses 29% less code by reversing the first relational operator. We allow the program to "fall through" to the second expression:

## Slide 19: Drill . . .
Implement the following pseudocode in assembly language. All values are unsigned:
  cmp ebx,ecx
  ja next
  cmp ecx,edx
  jbe next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx
&& ecx > edx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 20: Compound Expression with OR (1 of 2)
When implementing the logical OR operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is true, the second expression is skipped:
if (al > bl) OR (bl > cl)
X = 1;

## Slide 21: Compound Expression with OR (1 of 2)
cmp al,bl ; is AL > BL?
ja L1 ; yes
cmp bl,cl ; no: is BL > CL?
jbe next ; no: skip next statement
L1: mov X,1 ; set X to 1
next:
if (al > bl) OR (bl > cl)
X = 1;
We can use "fall-through" logic to keep the code as short as possible:

## Slide 22: WHILE Loops
while( eax < ebx)
eax = eax + 1;
A WHILE loop is really an IF statement followed by the body of the loop, followed by an unconditional jump to the top of the loop. Consider the following example:
top:cmp eax,ebx ; check loop condition
jae next ; false? exit loop
inc eax ; body of loop
jmp top ; repeat the loop
next:
This is a possible implementation:

## Slide 23: Drill . . .
top: cmp ebx,val1 ; check loop condition
ja next ; false? exit loop
add ebx,5 ; body of loop
dec val1
jmp top ; repeat the loop
next:
while( ebx <= val1)
{
ebx = ebx + 5;
val1 = val1 - 1
}
Implement the following loop, using unsigned 32-bit integers:

## Slide 24: Using the .IF Directive
Runtime Expressions
Relational and Logical Operators
MASM-Generated Code
.REPEAT Directive
.WHILE Directive

## Slide 25: Runtime Expressions
.IF eax > ebx
mov edx,1
.ELSE
mov edx,2
.ENDIF
.IF, .ELSE, .ELSEIF, and .ENDIF can be used to evaluate runtime expressions and create block-structured IF statements.
Examples:
MASM generates "hidden" code for you, consisting of code labels, CMP and conditional jump instructions.
.IF eax > ebx && eax > ecx
mov edx,1
.ELSE
mov edx,2
.ENDIF

## Slide 26: Relational and Logical Operators

## Slide 27: MASM-Generated Code
mov eax,6
cmp eax,val1
jbe @C0001
mov result,1
@C0001:
.data
val1 DWORD 5
result DWORD ?
.code
mov eax,6
.IF eax > val1
mov result,1
.ENDIF
Generated code:
MASM automatically generates an unsigned jump (JBE) because val1 is unsigned.

## Slide 28: MASM-Generated Code
mov eax,6
cmp eax,val1
jle @C0001
mov result,1
@C0001:
.data
val1 SDWORD 5
result SDWORD ?
.code
mov eax,6
.IF eax > val1
mov result,1
.ENDIF
MASM automatically generates a signed jump (JLE) because val1 is signed.
Generated code:

## Slide 29: MASM-Generated Code
mov ebx,5
mov eax,6
cmp eax,ebx
jbe @C0001
mov result,1
@C0001:
.data
result DWORD ?
.code
mov ebx,5
mov eax,6
.IF eax > ebx
mov result,1
.ENDIF
MASM automatically generates an unsigned jump (JBE) when both operands are registers . . .
Generated code:

## Slide 30: MASM-Generated Code
mov ebx,5
mov eax,6
cmp eax,ebx
jle @C0001
mov result,1
@C0001:
.data
result SDWORD ?
.code
mov ebx,5
mov eax,6
.IF SDWORD PTR eax > ebx
mov result,1
.ENDIF
. . . unless you prefix one of the register operands with the SDWORD PTR operator. Then a signed jump is generated.
Generated code:

## Slide 31: .REPEAT Directive
; Display integers 1 – 10:
mov eax,0
.REPEAT
inc eax
call WriteDec
call Crlf
.UNTIL eax == 10
Executes the loop body before testing the loop condition associated with the .UNTIL directive.
Example:

## Slide 32: .WHILE Directive
; Display integers 1 – 10:
mov eax,0
.WHILE eax < 10
inc eax
call WriteDec
call Crlf
.ENDW
Tests the loop condition before executing the loop body The .ENDW directive marks the end of the loop.
Example:

## Slide 33: Summary
Bit Test Instruction
  Copies bit n from an operand into the Carry flag
  Syntax: BT bitBase, n
Conditional LOOP Instructions
  LOOPZ and LOOPE
    LOOPZ/LOOPE destination
    Logic:
      ECX  ECX – 1
      if ECX > 0 and ZF=1, jump to destination
  LOOPNZ and LOOPNE
    LOOPZ/LOOPE destination
    Logic:
      ECX  ECX – 1
      if ECX > 0 and ZF=0, jump to destination

## Slide 34: Summary
Block Structures
  Block-Structured IF Statements
  Compound Expressions with AND
  Compound Expressions with OR
  WHILE Loops
  REPEAT Loops
(cont.)

## Slide 35: Reference
Most of the Slides are taken from Presentation:
Chapter 6
Assembly Language for Intel-Based Computers, 4th Edition
Kip R. Irvine
(c) Pearson Education, 2002. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.