## Slide 1: CSC332 – Data Security and Encryption
Dr. Adnan Ahmad
AdnanAhmad@ciitlahore.edu.pk

## Slide 2: Firewalls and Access Control Lists

## Slide 3: Firewalls
A filter that will let through only desirable interactions
A firewall is a computer (device or set of devices) that sits between your internal network and the rest of the network and attempts to prevent bad things from happening without preventing good things from happening
It is a system designed to prevent unauthorized access to or from a private network
Can be implemented in both hardware and software, or a combination of both

## Slide 4: Firewalls
Isolates an organization’s internal network from a larger external network, allowing some packets to pass, blocking others
A process that filters all traffic between a protected or “inside” network and a less trustworthy or “outside” network
administered
network
external network

## Slide 5: Firewalls
Firewalls implement a security policy (accept or deny), which distinguish “good” traffic from “bad” traffic
  Part of the challenge of protecting a network with a firewall is determining the security policy that meets the needs of the installation
Firewalls by Analogy
  Passports are (generally) checked at the border
  My office doesn’t have a door direct to the outside
  Bank still have vaults

## Slide 6: Why Use Firewalls
Firewalls centrally manage access to services in ways that individual systems should but don't
  Hosts have security holes
Firewalls can be professionally (and hence better) administered
They enforce the partition of a network into separate security domains
They can enforce policies such as systems outside the firewall can't access services on any systems inside the firewall
With such a restriction, even if the internal systems are more open than they should be or have bugs, they can't be attacked directly from systems outside the firewall

## Slide 7: Why Use Firewalls
Prevent denial of service attacks
  SYN flooding: attacker establishes many bogus TCP connections, no resources left for “real” connections
Prevent illegal modification/access of internal data
  e.g., attacker replaces CIA’s homepage with something else
Allow only authorized access to inside network
  set of authenticated users/hosts
Prevent insider attacks on critical systems
  Critical systems (human resources, payroll, etc.) can be hidden behind their own firewalls to prevent attacks from the inside

## Slide 8: Firewall Policies
By careful positioning of a firewall within a network, we can ensure that all network access that we want to control must pass through it
There are two main approaches to setting firewall policies regulating information flow
Default Permit:
  Conditions are specified that will result in data being blocked; any host or protocol not covered by these conditions will pass through by default
  Simpler to use, easy to configure, and more dangerous (you have to know everything that needs to be blocked)
Default Deny:
  The particular protocols allowed through and the hosts that may pass data or be contacted are specified; all others are denied
  Tends to be more secure

## Slide 9: Schematic of a Firewall
An “inside” everyone on the inside is presumed to be a good guy
An “outside” bad guys live there
A “DMZ” (Demilitarized Zone) put necessary but potentially dangerous servers there

## Slide 10: DMZ
Good spot for things like mail and web servers
  Firewalls protect administrative divisions
Outsiders can send email, retrieve web pages
Insiders can retrieve email, update web pages
Must monitor such machines very carefully

## Slide 11: Types of Firewalls
There are three main types of firewalls:
  State-less packet filters
  State-full packet filters
  Application gateways
They all work towards the same goals, but take different approaches in doing so

## Slide 12: State-less Packet Filters
Internal network connected to Internet (outside) via router firewall
Look at the headers of packets (accept/reject; no context is used), simplest and, in some situations, the most effective type of firewall
Router filters packet-by-packet
Decision to forward/drop packet based on:
  Source IP address, destination IP address
  TCP/UDP source and destination port numbers
  ICMP message type
  TCP SYN and ACK bits

## Slide 13: State-less Packet Filters
State-less Packet Filtering: Examples
Example 1: block incoming and outgoing datagrams with IP protocol field 17 and with either source or destination port 23
  All incoming, outgoing UDP flows and telnet connections are blocked
https://en.wikipedia.org/wiki/List_of_IP_protocol_numbers
https://en.wikipedia.org/wiki/List_of_TCP_and_UDP_port_numbers
Example 2: Block inbound TCP segments with ACK 0
  Prevents external clients from making TCP connections with internal clients, but allows internal clients to connect to outside

## Slide 14: State-less Packet Filters
State-less Packet Filtering: Examples
Policy: No outside Web access
Firewall Setting: Drop all outgoing packets to any IP address, port 80
Policy: No incoming TCP connections, except those for institution’s public Web server only
Firewall Setting: Drop all incoming TCP SYN packets to any IP except 130.207.244.203, port 80
Policy: Prevent your network from being trace-routed
Firewall Setting: Drop all outgoing ICMP TTL expired traffic

## Slide 15: State-less Packet Filters
State-less Packet Filtering: Examples
Policy: Prevent web-radios from eating up the available bandwidth
Firewall Setting: Drop all incoming UDP packets - except DNS and router broadcasts
Policy: Prevent your network from being used for a smurf DoS attack
Firewall Setting: Drop all ICMP packets going to a “broadcast” address (eg 130.207.255.255)

## Slide 16: State-full Packet Filters
State-less packet filter is not always good enough
Admits packets that “make no sense,” e.g., destination port 80, ACK bit set, even though no TCP connection established
State-full packet filter examine each IP packet “in context”
Keeping state means when a packet is sent out, record that
Associate inbound packet with state created by outbound packet

## Slide 17: State-full Packet Filters
Can track status of every TCP connection
  Track connection setup (SYN), teardown (FIN), can determine whether incoming, outgoing packets “makes sense”
  Timeout inactive connections at firewall, no longer admit packets
Keeps tracks of client-server sessions
Checks each packet validly belongs to one
Better able to detect bogus packets out of context
Solves many (but not all) of the problems with simple packet filters
Requires per-connection state in the firewall

## Slide 18: State-full Packet Filters
State-full Packet Filtering: Example
A state-full packet filter could, for instance, note that a connection was initiated from inside using IP address s, to IP address d, and then allow (for some period of time) connections from IP address d to IP address s
In the case of ftp, the state-full packet filter can notice when a connection is opened from s to the ftp control port (21) at d, and remember the incoming ftp data port (say p) requested by s
As long as the ftp control connection stays opened, the state-full packet filter will allow connections from the ftp data port (20) at d to port p at s

## Slide 19: Application Gateways
Filters packets on application data as well as on IP/TCP/UDP fields
  Look at the data inside the packets
Example: allow select internal users to telnet outside
Require all telnet users to telnet through gateway
For authorized users, gateway sets up telnet connection to destination host Gateway relays data between 2 connections
Router filter blocks all telnet connections not originating from gateway

## Slide 20: Application Gateways
Application Gateway Example:
A company wants to set up an on-line price list so that outsiders can see the products and prices offered
It wants to be sure that no outside can change the prices or product list and that outsiders can access only the price list, not any of the more sensitive files stored inside

## Slide 21: Application Gateways
A proxy server acts as the "man in the middle," so that there is no direct contact between a client on an internal network and a server on an untrusted network
Proxy has full access to the protocol
  User requests service from proxy
  Proxy validates request as legal
  Actions request and returns result to user

## Slide 22: Limitations of Firewalls
Firewalls can’t judge if data really comes from the claimed source (IP spoofing), so intruders may still be let in
Firewalls assumes that all the bad guys are on the outside, and everyone on the inside can be completely trusted
Firewalls often make it difficult for legitimate users to get their work done
If multiple applications need special treatment, each needs its own gateway

## Slide 23: Limitations of Firewalls
Client software must know how to contact the gateway
  For example, users must set the IP address of a proxy in their web browsers
Tradeoff, degree of communication with outside world, level of security
The more exceptions and specializations needed for a firewall, the harder it is to configure and get to work properly
Many highly protected sites still suffer from attacks, so are firewalls really the solution?

## Slide 24: Limitations of Firewalls
Should firewalls go away?
Even if the world deployed end-to-end security everywhere, firewalls still serve an important purpose
They can keep intruders from doing the equivalent of jiggling all the doors inside your building to see if someone accidentally left one unlocked
They can help protect against denial-of-service attacks by keeping nuisance traffic off your net

## Slide 25: Access Control Lists
Network administrators must figure out how to deny unwanted access to the network while allowing internal users appropriate access to necessary services
Although security tools, such as passwords, callback equipment, and physical security devices are helpful, they often lack the flexibility of basic traffic filtering and the specific controls most administrators prefer
For example, a network administrator may want to allow users access to the Internet, but not permit external users telnet access into the LAN
Routers provide basic traffic filtering capabilities, such as blocking Internet traffic, with access control lists (ACLs)
Access Lists have become powerful tools for controlling the behavior of packets and frames

## Slide 26: Access Control Lists
The goal of these filters (lists) is to prevent unwanted traffic in the network, whether to prevent hackers from penetrating the network or just to prevent employees from using systems they should not be using
IP access lists can also be used to filter routing updates, to match packets for prioritization, to match packets for VPN tunneling, and to match packets for implementing quality of service features

## Slide 27: Access Control Lists
ACLs
are read sequentially
are set up so that as soon as the packet matches a statement it stops comparing and permits or denies the packet
need to be written to take care of the most abundant traffic first
can be written for all supported routed protocols; but each routed protocol must have a different ACL for each interface
must be applied to an interface to work

## Slide 28: Access Control Lists
Only one list, per protocol, per direction can be applied to an interface
ACLs control traffic in one direction at a time on an interface
A separate ACL would need to be created for each direction, one for inbound and one for outbound traffic
Finally every interface can have multiple protocols and directions defined

## Slide 29: Access Control Lists
How ACLs Work
Access list statements operate in sequential, logical order
They evaluate packets from the top down
Once there is an access list statement match, the packet skips the rest of the statements
If a condition match is true, the packet is permitted or denied
There is an implicit “deny any” at the end of every access list
ACLs do not block packets that originate within the router (ie. pings, telnets, etc.)

## Slide 30: Access Control Lists
How ACLs Work
When an access lists applied to an inbound interface, the packets are checked against the access list before any routing table lookup process occurs
Outbound access lists are applied after the forwarding decision is made, after the routing table lookup process takes place and an exit interface is determined

## Slide 31: Access Control Lists
When writing an access list, the order of the lines is vital
The access list is compared to the packet on a line-by-line basis from top to bottom; once a match is found, the packet is either permitted or denied by the router
There is an "implied deny" for traffic that is not permitted
If there is no match, the implicit deny is applied to the packet
A single-entry ACL with only one "deny" entry has the effect of denying all traffic
You must have at least one "permit" statement in an ACL or all traffic will be blocked

## Slide 32: Access Control Lists
There are two types of IP ACLs: Standard and Extended
Standard IP ACLs can only control traffic based on the source IP address
Extended IP ACLs are far more powerful; they can identify traffic based on source IP, source port, destination IP, and destination port

## Slide 33: Access Control Lists
Standard Access Lists
filter (permit or deny) only source addresses
do not have any destination information so it must placed as close to the destination as possible
work at layer 3 of the OSI model

## Slide 34: Access Control Lists
Extended Access Lists
filter (permit or deny) based on the: source address, destination address, protocol and port number
are placed close to the source
work at both layer 3 and 4 of the OSI model

## Slide 35: THANKS