## Slide 1: Introduction
CSC 322: Operating Systems Concept

## Slide 2: A Typical Computer from Hardware Point of View
One or more CPUs and device controllers connected through common bus
Notes: A device controller is a part of a computer system that makes sense of the signals going to, and coming from the CPU. There are many device controllers in a computer system. Any device connected to the computer is connected by a plug and socket, and the socket is connected to a device controller.

## Slide 3: Computer System Components

## Slide 4: Example: Programming Hard Drive
Physical reality
  Block oriented
  Physical sector numbers
  No protection among user systems
  Data might be corrupted if machine crashes
  Programming:
    Loading values into special device registers
“I will save my lab1 solution on platter 5, track 8739, sector 3-4.”
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 5: Computer System Components
Managing all these components requires a layer of software – the operating system

## Slide 6: Example: Programming Hard Drive
Physical reality
  Block oriented
  Physical sector numbers
  No protection among user systems
  Data might be corrupted if machine crashes
  Programming:
    Loading values into special device registers
“I will save my lab1 solution on platter 5, track 8739, sector 3-4.”
File system abstraction
  Byte oriented
  Named files
  User protected from each other
  Robust to machine failures
  Programming:
    open/read/write
“My lab1 solution is in ~mhjamal/lab1/process.c.”
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 7: Computer System Structure
Computer system can be divided into four components:
  Hardware – provides basic computing resources
    CPU, memory, I/O devices
  Operating system
    Controls and coordinates use of hardware among various applications and users
  Application programs – define the ways in which the system resources are used to solve the computing problems of the users
    Word processors, compilers, web browsers, database systems, video games
  Users
    People, machines, other computers

## Slide 8: Computer Startup
Bootstrap program is loaded at power-up or reboot
  Typically stored in ROM or EEPROM, generally known as firmware
  Initializes all aspects of system
  Locates and loads operating system kernel into memory and starts execution
  Sometimes two-step process where boot block at fixed location loaded by ROM code, which loads bootstrap loader from disk
Common bootstrap loader, GRUB, allows selection of kernel from multiple disks, versions, kernel options
Kernel loads and system is then running

## Slide 9: Computer Startup
ROM/BIOS contains firmware responsible to initiate the function of the computer.
This firmware
  IPL (Initial Program Loader) is the first program which is executed whenever computer is turned ON.
  ROM/BIOS is the first chip which is turned ON.
IPL checks the presence of the storage device.
Then to go to search OS on it.
If no OS then “No boot device available” message displayed by IPL.

## Slide 10: Computer Startup
If storage device present then
  IPL executes the boot strap routines (stored on the boot sector of HDD)
  BOOT Sector is the first sector of the first track
  Boot Strap Routines
    Load the OS into the computer memory.
    Finds the OS kernel on the HDD,
    Load into memory and
    Jumps to the initial address to begin the OS’s execution.

## Slide 11: Brief History of Computer Systems
In the beginning 1 user/program at a time
Simple batch systems were 1st real OS
  Spooling and buffering allowed jobs to be read ahead of time
Multiprogramming systems provided increased utilization (throughput)
  Multiple runnable jobs loaded in memory
  Overlap I/O with computation
  Benefit from asynchronous I/O devices
  1st instance where the OS must schedule resources
    CPU scheduling
    Memory management
    Protection
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 12: Brief History of Computer Systems
Timesharing (Multitasking) is a logical extension of multiprogramming
  Optimize response time by frequent time-slicing multiple jobs
  Each user feels he/she has the entire machine
  Permits interactive work
  More complex than the multiprogramming OS
    In addition to CPU scheduling, memory management, protection
    Virtual memory to allow part of the job to be in memory
    File system (needed by interactive use)
    Job communication, synchronization
    Handling deadlock
  Most systems today are timesharing (focus of this course)
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 13: What is an Operating System?
“Code” that sits between:
  Programs & hardware
  Different programs
  Different users
A program that acts as an intermediary between a computer user and the computer hardware
  High level interface between user and machine
But what does it do/achieve?
  Execute user programs and make solving user problems easier
  Make the computer system convenient to use
  Use the computer hardware in an efficient manner
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 14: What is an Operating System?
Resource Manager
Extended (abstract) machine
Makes computers efficient and simple to use
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 15: What is an Operating System?
Resource Manager
  Allocation
  Reclamation
  Protection
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 16: What is an Operating System?
Resource Manager
  Allocation
  Reclamation
  Protection
Finite resources
Competing demands
Examples:
CPU
Memory
Disk
Network
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 17: What is an Operating System?
Resource Manager
  Allocation
  Reclamation
  Protection
“The OS giveth
The OS taketh away”
Implied at termination
Involuntary at run time
Cooperative (yield CPU)
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 18: What is an Operating System?
Resource Manager
  Allocation
  Reclamation
  Protection
“You can’t hurt me
I can’t hurt you”
Implies some degree of safety & security
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 19: What is an Operating System?
Operating System as a resource manager
  Allow multiple programs to run at the same time
  Manage and protect memory, I/O devices, and other resources
  Includes multiplexing (sharing) resources in two different ways:
    In time
    In space
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 20: What is an Operating System?
Extended (abstract) machine
  Much more ideal environment than the hardware
    Ease of use
    Fair (well-behaved)
    Portable (back-compatible)
    Reliable
    Safe
  Illusion of infinite, private resources
    Single processor  many separate processors
    Single memory  many separate, larger memories
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 21: Separating Policy from Mechanism
A fundamental design principle in Computer Science
Mechanism – tool/implementation to achieve some effect
Policy – decisions on what effect should be achieved
  Examples:
    All users treated equally
    All programs instances treated equally
    Preferred users treated better
Separation leads to flexibility
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 22: Is there a perfect OS?
Fairness
Efficiency
Portability
Interfaces
Security
Robustness
Conflicting goals
  Fairness vs efficiency
  Efficiency vs portability
  …
Furthermore, …
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 23: Hardware is evolving …
60’s – 70’s  Mainframes
  Rise of IBM
70’s – 80’s  Minicomputers
  Rise of Digital Equipment
80’s – 90’s  PCs
  Rise of Intel, Microsoft
90’s – today  Handheld systems (smartphones)
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 24: Computer Hardware Review: Processors
Instruction Set
  Pentium cannot execute SPARC programs
ALU Arithmetic/Logic Unit
Instruction Register
  address of the next instruction to be fetched
Stack Pointer
  points to the top of the current stack in memory
General Registers
PSW Program Status Word
  condition code bits, which are set by comparison instructions
Pipeline
Note: CPUs contain some registers inside to hold key variables and temporary results

## Slide 25: Computer Hardware Review: Processors
(a) A three-stage pipeline. (b) A superscalar CPU.

## Slide 26: Historical Comparison
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 27: Hardware is evolving …
New architectures
  32-bit vs 64 bit
  Multiprocessors
  Multi-core
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 28: May You Live in Interesting Times …
Processor speed doubles in 18 months
  Number of cores per chip doubles in 24 months
Disks capacity doubles every 12 months
Performance/cost “sweet spot” constantly decaying
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 29: Applications are also evolving
New applications
  Computer games
  Java
  WWW (web servers)
  Networked games
  Peer-to-peer
  Web 2.0 (Youtube, social network)
  Mobile device applications
  …
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 30: There is no magic in OS design
This is Engineering
  Imperfection
  Tradeoffs (perf/func)
  Constraints
    Hardware, cost, time, power
Optimizations
Nothing is permanent
High rate of change
  Hardware
  Applications
Cost/benefit analyses
One good news:
  Inertia of a few design principles
Notes: An operating system is a program that manages the computer hardware. It also provides a basis for application programs and acts as an intermediary
between a user of a computer and the computer hardware.

## Slide 31: Storage Definitions and Notation Review
The basic unit of computer storage is the bit. A bit can contain one of two values, 0 and 1. All other storage in a computer is based on collections of bits. Given enough bits, it is amazing how many things a computer can represent: numbers, letters, images, movies, sounds, documents, and programs, to name a few. A byte is 8 bits, and on most computers it is the smallest convenient chunk of storage. For example, most computers don’t have an instruction to move a bit but do have one to move a byte. A less common term is word, which is a given computer architecture’s native unit of data. A word is made up of one or more bytes. For example, a computer that has 64-bit registers and 64-bit memory addressing typically has 64-bit (8-byte) words. A computer executes many operations in its native word size rather than a byte at a time.
Computer storage, along with most computer throughput, is generally measured and manipulated in bytes and collections of bytes.
A kilobyte, or KB, is 1,024 bytes
a megabyte, or MB, is 1,0242 bytes
a gigabyte, or GB, is 1,0243 bytes
a terabyte, or TB, is 1,0244 bytes
a petabyte, or PB, is 1,0245 bytes
Computer manufacturers often round off these numbers and say that a megabyte is 1 million bytes and a gigabyte is 1 billion bytes. Networking measurements are an exception to this general rule; they are given in bits (because networks move data a bit at a time).

## Slide 32: Storage Hierarchy
Storage systems organized in hierarchy
  Speed
  Cost
  Volatility

## Slide 33: Storage Structure
Main memory – only large storage media that the CPU can access directly
  Random access
  Typically volatile
Secondary storage – extension of main memory that provides large nonvolatile storage capacity
Hard disks – rigid metal or glass platters covered with magnetic recording material
  Disk surface is logically divided into tracks, which are subdivided into sectors
  The disk controller determines the logical interaction between the device and the computer
Solid-state disks – faster than hard disks, nonvolatile
  Various technologies
  Becoming more popular
Caching – copying information into faster storage system; main memory can be viewed as a cache for secondary storage
Device Driver for each device controller to manage I/O
  Provides uniform interface between controller and kernel

## Slide 34: Caching
Important principle, performed at many levels in a computer
  in hardware, operating system, software
Information in use copied from slower to faster storage temporarily
Faster storage (cache) checked first to determine if information is there
  If it is, information used directly from the cache (fast)
  If not, data copied to cache and used there
Cache smaller than storage being cached
  Cache management important design problem
  Cache size and replacement policy

## Slide 35: Performance of Various Levels of Storage

## Slide 36: Migration of data “A” from Disk to Register
Multitasking environments must be careful to use most recent value, no matter where it is stored in the storage hierarchy
Multiprocessor environment must provide cache coherency in hardware such that all CPUs have the most recent value in their cache
Distributed environment situation even more complex
  Several copies of a datum can exist
  Various solutions covered in Chapter 17

## Slide 37: I/O Subsystem
One purpose of OS is to hide peculiarities of hardware devices from the user
I/O subsystem responsible for
  Memory management of I/O including buffering (storing data temporarily while it is being transferred), caching (storing parts of data in faster storage for performance), spooling (the overlapping of output of one job with input of other jobs)
  General device-driver interface
  Drivers for specific hardware devices

## Slide 38: Protection and Security
Protection – any mechanism for controlling access of processes or users to resources defined by the OS
Security – defense of the system against internal and external attacks
  Huge range, including denial-of-service, worms, viruses, identity theft, theft of service
Systems generally first distinguish among users, to determine who can do what
  User identities (user IDs, security IDs) include name and associated number, one per user
  User ID then associated with all files, processes of that user to determine access control
  Group identifier (group ID) allows set of users to be defined and controls managed, then also associated with each process, file
  Privilege escalation allows user to change to effective ID with more rights

## Slide 39: Direct Memory Access Structure
Used for high-speed I/O devices able to transmit information at close to memory speeds
Device controller transfers blocks of data from buffer storage directly to main memory without CPU intervention
Only one interrupt is generated per block, rather than the one interrupt per byte

## Slide 40: How a Modern Computer Works
A von Neumann architecture

## Slide 41: Computer-System Architecture
Most systems contain a single general-purpose processor
  Few systems contain special-purpose processors as well
Multiprocessors systems growing in use and importance
  Also known as parallel systems, tightly-coupled systems
  Advantages include:
    Increased throughput- more work done in less time
      Speed up ratio with N processor is not N
        Overhead of keeping all component working correctly
        Contention for shared resources
    Economy of scale
    Increased reliability – graceful degradation or fault tolerance
      The ability of a system to maintain limited functionality even when a large portion of it has been destroyed or rendered inoperative

## Slide 42: Computer-System Architecture
  Multiprocessor systems are of two types:
    Asymmetric Multiprocessing– each processor assigned a specific task
      Master-slave relationship
      The tasks are strictly divided by their types on processors
      Typically, each processor has its own memory address space
      These features make asymmetric multiprocessing difficult to implement.
    Symmetric Multiprocessing (SMP)– each processor performs all tasks within the OS or they can do anything the others can.
      All processor are peers
      Contain own set of registers and private or local caches
      Shared physical memory
Asymmetric multiprocessing; one processor doing all I/O
Symmetric multiprocessing

## Slide 43: A Dual-Core Design
  Cores- Multiprocessor chips
    on-chip communication is faster
    well suited for server (i.e., database, Web servers)
    Multicore CPUs appear to the operating system as N standard processors
A dual-core design with two cores places on the same chip

## Slide 44: Multithreaded and Multicore Chips
(a) A quad-core chip with a shared L2 cache.
(b) A quad-core chip with separate L2 caches.

## Slide 45: Clustered Systems
Another type of multiple-CPU system is clustered system
  Usually sharing storage via a storage-area network (SAN)
  Provides a high-availability service which survives failures
    Asymmetric clustering; One machine in hot-standby mode while the other is running the applications
    Symmetric clustering; multiple machines are running the applications as well as monitoring each other
  Some clusters are for high-performance computing (HPC)
    Applications must be written to use parallelization

## Slide 46: Computing Environments - Traditional
Stand-alone general-purpose machines
But blurred as most systems interconnect with others (i.e., the Internet)
Network computers (thin clients) are like Web terminals
Mobile computers interconnect via wireless networks
Networking becoming ubiquitous – even home systems use firewalls to protect home computers from Internet attacks
Single User, single task OS (e.g., PDA and MS-DOS)
Single User, Multitasking OS (Microsoft's Windows and Apple's Mac OS)
Multiuser OS (Unix, VMS and mainframe operating systems)
  Allows multiple users to use computer's resources simultaneously in a balanced manner, provided sufficient resources
Batch OS
  No interaction of user with the computer directly. Job is prepared on an offline device like punch cards and submitted to the computer operator.

## Slide 47: Computing Environments - Mobile
Mobile OS
  Controls a mobile device and its design to supports wireless communication and mobile applications.
  Has built-in support for mobile multimedia formats. Tablet PCs and smart phones run on mobile operating systems.
  Allows new types of apps like augmented reality
  Leaders are Apple iOS and Google Android

## Slide 48: Computing Environments – Distributed
Distributed Computing
  Collection of independent, possibly heterogeneous, systems networked together
    Network is a communications path, TCP/IP most common
      Local Area Network (LAN)
      Wide Area Network (WAN)
      Metropolitan Area Network (MAN)
      Personal Area Network (PAN)
Distributed Operating System provides features between systems across network
  Communication scheme allows systems to exchange messages
  Computations are carried out on more than one machine
  Illusion of a single system

## Slide 49: Computing Environments – Client-Server
Client-Server Computing
  Dumb terminals supplanted by smart PCs
  Many systems now servers, responding to requests generated by clients
    Compute-server system provides an interface to client to request services (i.e., database)
    File-server system provides interface for clients to store and retrieve files

## Slide 50: Computing Environments - Peer-to-Peer
Another model of distributed system
P2P does not distinguish clients and servers
  Instead all nodes are considered peers
  May each act as client, server or both
  Node must join P2P network
    Registers its service with central lookup service on network, or
    Broadcast request for service and respond to requests for service via discovery protocol
  Examples include Napster and Gnutella, Voice over IP (VoIP) such as Skype

## Slide 51: Computing Environments - Virtualization
Allows operating systems to run applications within other OSes
  Vast and growing industry
Emulation used when source CPU type different from target type (i.e. PowerPC to Intel x86)
  Generally slowest method
  When computer language not compiled to native code – Interpretation
Virtualization – OS natively compiled for CPU, running guest OSes also natively compiled
  Consider VMware running WinXP guests, each running applications, all on native WinXP host OS
  VMM (virtual machine Manager) provides virtualization services

## Slide 52
Use cases involve laptops and desktops running multiple OSes for exploration or compatibility
  Apple laptop running Mac OS X host, Windows as a guest
  Developing apps for multiple OSes without having multiple systems
  QA testing applications without having multiple systems
  Executing and managing compute environments within data centers
VMM can run natively, in which case they are also the host
  There is no general-purpose host then (VMware ESX and Citrix XenServer)
Computing Environments - Virtualization

## Slide 53: Computing Environments – Cloud Computing
Delivers computing, storage, even apps as a service across a network
Logical extension of virtualization because it uses virtualization as the base for its functionality.
  Amazon EC2 has thousands of servers, millions of virtual machines, petabytes of storage available across the Internet, pay based on usage
Many types
  Public cloud – available via Internet to anyone willing to pay
  Private cloud – run by a company for the company’s own use
  Hybrid cloud – includes both public and private cloud components
  Software as a Service (SaaS) – one or more applications available via the Internet (i.e., word processor)
  Platform as a Service (PaaS) – software stack ready for application use via the Internet (i.e., a database server)
  Infrastructure as a Service (IaaS) – servers or storage available over Internet (i.e., storage available for backup use)

## Slide 54
Cloud computing environments composed of traditional OSes, plus VMMs, plus cloud management tools
  Internet connectivity requires security like firewalls
  Load balancers spread traffic across multiple applications
Computing Environments – Cloud Computing

## Slide 55: Computing Environments – RTOS
Real-time embedded systems most prevalent form of computers
  Vary considerable, special purpose, limited purpose OS, Real-Time OS (RTOS)
  Used to control machinery, scientific instruments and industrial systems
  Its use is expanding
Many other special computing environments as well
  Some have OSes, some perform tasks without an OS
  Very little user-interface capability, and no end-user utilities, since the system will be a "sealed box" when delivered for use (e. g., HDTV receiver and display)
Real-time OS has well-defined fixed time constraints
  Processing must be done within constraint (must be quick)
  Correct operation only if constraints met
  Predictable response to events.

## Slide 56: Open-Source Operating Systems
Operating systems made available in source-code format rather than just binary closed-source
Counter to the copy protection and Digital Rights Management (DRM) movement
Started by Free Software Foundation (FSF), which has “copyleft” GNU Public License (GPL)
Examples include GNU/Linux and BSD UNIX (including core of Mac OS X), and many more
Can use VMM like VMware Player (Free on Windows), Virtualbox (open source and free on many platforms - http://www.virtualbox.com)
  Use to run guest operating systems for exploration

## Slide 57: Available Operating Systems in the market
Notes: Berkeley Software Distribution (BSD) is a Unix operating system derivative developed and distributed by the Computer Systems Research Group (CSRG) of the University of California, Berkeley, from 1977 to 1995.
Symbian was a mobile operating system (OS) and computing platform designed for smartphones.
z/OS is a 64-bit operating system for IBM mainframes, produced by IBM. It derives from and is the successor to OS/390, which in turn followed a string of MVS versions.