## Slide 1: Data Link Layer
Imran Raza
Computer Networks Research Center (CNRC)
Computer Science Department, CIIT, Lahore.
http://research.ciitlahore.edu.pk/Groups/CNRC/

## Slide 2: Agenda
Link Layer Review
Link Layer Services
Error Detection
Error Correction
Multiple Access Control Protocols

## Slide 3: Link Layer: Review
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 PDU is a frame, encapsulates datagram
“link”
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 4: Link layer: Review…
Datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
Each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link

## Slide 5: Link Layer Services: Review
Framing, link access
Reliable delivery between adjacent nodes
Flow Control
Error Detection
Error Correction
Half-duplex and full-duplex

## Slide 6: Error Detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction

## Slide 7: Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0

## Slide 8: Two Dimensional Parity

## Slide 9: Example
Suppose the following block is sent:
10101001 00111001 11011101 11100111 10101010
However, it is hit by a burst noise of length 8, and some bits are corrupted.
10100011 10001001 11011101 11100111 10101010
When the receiver checks the parity bits, some of the bits do not follow the even-parity rule and the whole block is discarded.
10100011 10001001 11011101 11100111 10101010

## Slide 10: Cyclic Redundancy Check/Polynomial Codes
A (n+1)-bit message can be represented as a polynomial of degree n. For example,
  X = 10011010;
  M(X) =
So, a sender and receiver can be considered to exchange polyns.
Choose k+1 bit pattern (divisor), C(X), a polyn of degree k
goal: choose k CRC bits, R, such that
  <M,R> exactly divisible by C (modulo 2)
  receiver knows C, divides <M,R> by C. If non-zero remainder: error detected!
  can detect all burst errors less than k+1 bits

## Slide 11: CRC continued …
Goal: design P(X) such that it is exactly divisible by C(X)
Multiply M(X) by xk (add k zero’s to the end of the message) to get T(X)
Divide T(X) by C(X) and find the remainder R(X)
Subtract the remainder from T(X) to get P(X). P(X) is now exactly divisible by C(X).
Remember – all addition/subtract use modulo-2 arithmetic.

## Slide 12: CRC- example

## Slide 13: CRC- example…

## Slide 14: Standard Polynomials
Name | Polynomial | Application
CRC-8 | x8 + x2 + x + 1 | ATM header
CRC-10 | x10 + x9 + x5 + x4 + x 2 + 1 | ATM AAL
ITU-16 | x16 + x12 + x5 + 1 | HDLC
ITU-32 | x32 + x26 + x23 + x22 + x16 + x12 + x11 + x10 + x8 + x7 + x5 + x4 + x2 + x + 1 | LANs

## Slide 15: Checksum

## Slide 16: Checksum-example
Suppose the following block of 16 bits is to be sent using a checksum of 8 bits.
10101001 00111001
The numbers are added using one’s complement
10101001
00111001 ------------ Sum 11100010
Checksum 00011101
The pattern sent is 10101001 00111001 00011101

## Slide 17: Checksum-example (receiver side)
Now suppose the receiver receives the pattern sent in Example 7 and there is no error.
10101001 00111001 00011101
When the receiver adds the three sections, it will get all 1s, which, after complementing, is all 0s and shows that there is no error.
10101001
00111001
00011101
Sum 11111111
Complement 00000000 means that the pattern is OK.

## Slide 18: Error Correction
Retransmission
Forward Error Correction

## Slide 19: Forward Error Correction
Number of data bits m | Number of redundancy bits r | Total bits m + r
1 | 2 | 3
2 | 3 | 5
3 | 3 | 6
4 | 3 | 7
5 | 4 | 9
6 | 4 | 10
7 | 4 | 11

## Slide 20: Forward Error Correction –Hamming Code

## Slide 21: Hamming Code-redundancy bits calculations

## Slide 22: Hamming Code-redundancy bits calculations…

## Slide 23: Error detection using hamming code

## Slide 24: Multiple Access Links and Protocols
Two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch and host
broadcast (shared wire or medium)
  traditional Ethernet
  upstream HFC
  802.11 wireless LAN

## Slide 25: When are Multiple Access Protocols Required?
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time (examples, LANs, Wireless-LANs)
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 26: Ideal Multiple Access Protocol
Broadcast channel of rate R bps
1. When one node wants to transmit, it can send at rate R.
2. When M nodes want to transmit, each can send at average rate R/M
3. Fully decentralized:
  no special node to coordinate transmissions
  no synchronization of clocks, slots
4. Simple and easy to implement

## Slide 27: Taxonomy of Multiple Access Control Protocols
Three broad classes:
Channel Partitioning
  divide channel into smaller “pieces” (TDM, FDM, Code Division Multiple Access) – TDM, FDM covered in previous lec.
  allocate piece to node for exclusive use
Random Access
  channel not divided, allow collisions
  “recover” from collisions
“Taking turns”
  Nodes take turns, but nodes with more to send can take longer turns

## Slide 28: Random Access Protocols
When node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 29: Pure ALOHA
Let nodes transmit whenever a frame arrives
No synchronization among nodes
  If collision, retransmit after random delay
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 30: Pure Aloha efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [p0-1,p0] .
P(no other node transmits in [p0-1,p0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n -> infty ...
= 1/(2e) = .18

## Slide 31: Slotted ALOHA
Assumptions
all frames same size
time is divided into equal size slots, time to transmit 1 frame
nodes start to transmit frames only at beginning of slots
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
Operation
when node obtains fresh frame, it transmits in next slot
no collision, node can send new frame in next slot
if collision, node retransmits frame in each subsequent slot with prob. p until success

## Slide 32: Slotted ALOHA
Pros
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons
collisions, wasting slots
idle slots
clock synchronization

## Slide 33: Slotted Aloha efficiency
Suppose N nodes with many frames to send, each transmits in slot with probability p
prob that node 1 has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
For max efficiency with N nodes, find p* that maximizes Np(1-p)N-1
For many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives 1/e = .37
Efficiency is the long-run fraction of successful slots when there are many nodes, each with many frames to send
At best: channel
used for useful
transmissions 37%
of time!

## Slide 34: Carrier Sense Multiple Access (CSMA)
First listen; transmit only if channel sensed to be idle
Can collisions occur in this scheme?
  One possibility: two nodes might attempt to transmit a frame at the same time
  Another possibility?

## Slide 35: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: receiver shut off while transmitting

## Slide 37: CSMA\CD-Efficiency
tprop = max prop between 2 nodes in LAN
ttrans = time to transmit max-size frame
Efficiency goes to 1 as tprop goes to 0
Goes to 1 as ttrans goes to infinity
Much better than ALOHA, but still decentralized, simple, and cheap

## Slide 38: Time-Space Diagram of Two CSMA nodes

## Slide 39: CSMA with collision detection

## Slide 40
CSMA/CA flowchart

## Slide 41: CSMA\CA

## Slide 42: CSMA\CA

## Slide 43: CSMA\CA- Fragment Burst

## Slide 44: CSMA\CA-Inter frame Spaces

## Slide 45: MAC Architecture

## Slide 46: Transmission of MPDU without RTS\CTS

## Slide 47: Fragmented MPDU

## Slide 51: “Taking Turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 52: “Taking Turns” MAC protocols
Polling:
master node “invites” slave nodes to transmit in turn
concerns:
  polling overhead
  latency
  single point of failure (master)
Token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)

## Slide 53: Summary of MAC protocols
What do you do with a shared media?
  Channel Partitioning, by time, frequency or code
    Time Division, Frequency Division
  Random partitioning (dynamic),
    ALOHA, S-ALOHA, CSMA, CSMA/CD
    carrier sensing: easy in some technologies (wire), hard in others (wireless)
    CSMA/CD used in Ethernet
    CSMA/CA used in 802.11
  Taking Turns
    polling from a central site, token passing

## Slide 54: Ethernet

## Slide 55: Ethernet introduction
Ethernet is the most widely used local area network (LAN) technology.
Ethernet was designed to carry data at high speeds for very limited distances.
Ethernet is well suited to applications where a local communication medium must carry sporadic, occasionally heavy traffic at high peak data rates.

## Slide 56: Ethernet history
1960s, the University of Hawaii.
1970s, Xerox developed the first system.
1980, IEEE released 802.3 specification.
1980s, Digital, Intel and Xerox jointly developed and released an Ethernet specification (v2.0), Compatible with 802.3
Today, the term Ethernet is often used to refer to Ethernet specifications, including IEEE 802.3.

## Slide 57: Datalink and Physical layers

## Slide 58: Comparing Ethernet and IEEE 802.3
Specify similar technologies.
Broadcast network.
Using CSMA/CD algorithm.
Hardware implementation.
Differences:
  Ethernet provides services corresponding to physical and datalink layer.
  IEEE 802.3 specifies the physical layer and the channel-access portion of the data link layer but does not define a LLC protocol.

## Slide 59: Ethernet family

## Slide 60: Ethernet frame format

## Slide 61: Preamble
Note that a frame is Ethernet or IEEE 802.3.

## Slide 62: Start of frame delimiter (SOF)
The IEEE 802.3: synchronize the frame-reception portions of all stations on the LAN.
Be explicitly specified in Ethernet.

## Slide 63: Source and destination addresses
MAC addresses.
Unicast.
Multicast (D)
Broadcast (D)

## Slide 64: Type (Ethernet)
Specifies the upper-layer protocol to receive the data after Ethernet processing is completed

## Slide 65: Length (IEEE 802.3)
The length indicates the number of bytes of data that follows this field

## Slide 66: Data (Ethernet)
the data contained in the frame is sent to an upper-layer protocol

## Slide 67: Data (IEEE 802.3)
Data send to LLC layer, including LLC header and upper-layer data

## Slide 68: Frame check sequence (FCS)
This sequence contains a 4 byte CRC value that is created by the sender and is recalculated by the receiver to check for damaged frames

## Slide 69: Ethernet MAC Sublayer Protocol (2)

## Slide 70: Encoding: Manchester T+/-

## Slide 71: Switched Ethernet
A simple example of switched Ethernet.

## Slide 72: Review
Ethernet differences from IEEE 802.3.
Ethernet and IEEE 802.3 frame structure.
Encoding and topology.

## Slide 73: Reference
Lecture Slides of Jim F. Kurose (Chapter 5)
Lecture Slides of Behrouz A. Farouzan (Chapter 10)
Cisco Resources

## Slide 74: Deterministic LAN Technologies: Token Ring & FDDI

## Slide 75: Token Ring and variants
IBM developed the first Token Ring network in the 1970s. It is still IBM's primary LAN technology, and is second only to Ethernet (IEEE 802.3) in terms of LAN implementation.

## Slide 76: Ring topology

## Slide 77: Data passing
When a station has information to transmit, it seizes the token and sends data frame to the next station.
When frame reaches the destination station, the data is copied for processing.
Frame continues to circle the ring until it returns to the sending station.
Sending station removes the frame from the ring, verifies receipt, and releases the token.

## Slide 78: Token-Ring frame format

## Slide 79: Start delimiter and End delimiter
Start delimiter.
  Alert for the arrival of a token.
  Includes an identification symbol.
End Delimiter
  Completes the token or data/command frame.
  Contains damage indicator.
  Last of logical sequence.

## Slide 80: Access control
P: Priority bits
T: Token bit
M: Monitor bit
R: Reservation bits
P
P
P
T
M
R
R
R

## Slide 81: Priority and reservation bits
B'000' Normal User Priority
B'001' Normal User Priority
B'010' Normal User Priority
B'011' Normal User priority
B'100' Bridge/Router
B'101' Reserved IBM
B'110' Reserved IBM
B'111' Station Management

## Slide 82: Priority management
Using the priority field and the reservation field.
Stations with a higher priority can reserve the token for the next network pass.
Stations that raise a token's priority level must reinstate the previous priority after their transmission has been completed.

## Slide 83: Frame control
Only present in data/command frames.
Indicates whether frame contains data or control information.
If control, this byte specifies type of control information.

## Slide 84: Destination and Source addresses
Universal Address.
Local Administered Address.
Broadcast Address (D).

## Slide 85: Data
Length limited by the maximum time a station may hold the token.

## Slide 86: Frame checksum
Frame Check Sequence.
Source fills field with calculated value dependent on frame contents.
Destination recalculates to check data integrity.
Frame is discarded if damaged.

## Slide 87: Frame status
Address recognized / frame copied indicator.

## Slide 88: Management mechanisms
Active Monitor
  One station acts as centralized source of timing information for other stations.
  Removes continuously circulating frames by set monitor bit to 1.
  Start a token, when token have been lost.
Beaconing
  Detects and repairs network faults.
  Initiates auto-reconfiguration.

## Slide 89: Encoding: Differential Manchester

## Slide 90: Physical topology
Physical topology : Star.
Logical topology : Ring.
IBM Token Ring network stations are connected to MSAU (Multi-Station Access Unit).
Many MSAU can be wired together to form one large ring.

## Slide 91: Physical connection

## Slide 92: Review
Operation of Token-Ring.
Token-Ring frame structure.
Encoding and topology.

## Slide 93: BASIC OF FDDI

## Slide 94: Characteristics
Fiber Distributed Data Interface.
FDDI is popular as a campus backbone technology.
100 Mbps
Token passing
Dual-ring
Fiber Optic Cable
Total fiber length of 200Km
Station distances up to 2Km

## Slide 95: FDDI dual-ring (PR and SR)

## Slide 96: FDDI Media
Fiber Optic
  Single-mode, Laser (< 40Km)
  Multi-mode, LED (< 2Km)
  Multi-mode low cost, LED (< 500m)
Twisted Pair Copper
  UTP, STP (< 100m)

## Slide 97: Fiber-optic modes

## Slide 98: FDDI Connections
Class A: connect directly with PR – SR.
  DAC: Dual Attachment Concentrator
  DAS: Dual Attachment Station
Class B: connect via FDDI concentrator.
  SAS: Single Attachment Station

## Slide 99: Attachments

## Slide 100: FDDI standard: ANSI X3T9.5

## Slide 101: Physical Layer Medium (PMD)
Physical Medium Dependent:
How a station physically connect to a FDDI ring?
Defines the characteristics of the transmission medium:
  Fiber optic link
  Power levels
  Bit error rates
  Optical components
  Connectors

## Slide 102: Physical Layer Protocol (PHY)
PHysical laYer protocol:
How the signals are transmitted around the FDDI ring?
Part of the physical layer that are media independent.
Defines data encoding/decoding procedures:
  Framing
  Clocking requirements
  Other functions (Link state…)

## Slide 103: Media Access Control (MAC)
Media Access Control:
How the physical medium is accessed on FDDI ring?
Construction, transmission, receiving, and removal of frames and tokens.
Defines how the medium is accessed:
  Frame format
  Token handling
  Addressing
  Error recovery mechanisms

## Slide 104: Station Management (SMT)
Defines the FDDI station configuration, enables stations to work together within the ring :
  Ring configuration
  Initialization
  Station insertion and removal
  Fault isolation and recovery
  Scheduling
  Collection of statistics

## Slide 105: FDDI frame format

## Slide 106: Preamble, Start and End delimiter
Preamble.
  Prepares for the upcoming frame
Start delimiter.
  Alert for the arrival of a token.
  Differentiate from other frame fields.
End Delimiter
  Completes the frame.
  Contains damage indicator.

## Slide 107: Frame control
The size of the address fields
Other control information
Asynchronous or Synchronous data

## Slide 108: Source and destination addresses
Addresses are 6 bytes
Unicast
Multicast (D)
Broadcast (D)

## Slide 109: Data
Control information, or information destined for an upper-layer protocol

## Slide 110: FCS
Cyclic redundancy check (CRC).
For error control

## Slide 111: Frame status
Allows the source station to determine if an error occurred and if the frame was recognized and copied by a receiving station

## Slide 112: Operation mechanisms
Connection Establishment
  Station connect to neighbors to form the ring.
  Negotiate the length of the link.
Ring Initialization
  Station claim the right to generate a token.
Steady-state Operation
  Token passing
Ring Maintenance
  Detects and repairs token or network faults.

## Slide 113: Encoding: 4B/5B

## Slide 114: FDDI topology

## Slide 115: Review
Operation of FDDI.
FDDI frame structure.
Encoding and topology.

## Slide 116: LAN Addresses and ARP
32-bit IP address:
network-layer address
used to get datagram to destination IP network (recall IP network definition)
LAN (or MAC or physical or Ethernet) address:
used to get datagram from one interface to another physically-connected interface (same network)
48 bit MAC address (for most LANs) burned in the adapter ROM

## Slide 117: LAN Addresses and ARP
Each adapter on LAN has unique LAN address

## Slide 118: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address
MAC flat address => portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  depends on IP network to which node is attached

## Slide 119: Recall Encapsulation
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B, find B on same net. as A
link layer send datagram to B inside link-layer frame
B’s MAC
addr
A’s MAC
addr
A’s IP
addr
B’s IP
addr
IP payload
datagram
frame
frame source,
dest address
datagram source,
dest address

## Slide 120: ARP: Address Resolution Protocol
Each IP node (Host, Router) on LAN has ARP table
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
MAC address of B
knowing B’s IP address?

## Slide 121: ARP protocol
A wants to send datagram to B, and A knows B’s IP address.
Suppose B’s MAC address is not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  all machines on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 122: Routing to another LAN
walkthrough: send datagram from A to B via R
assume A knows B IP address
Two ARP tables in router R, one for each IP network (LAN)
In routing table at source Host, find router 111.111.111.110
In ARP table at source, find MAC address E6-E9-00-17-BB-4B, etc
A
R
B

## Slide 123
A creates datagram with source A, destination B
A uses ARP to get R’s MAC address for 111.111.111.110
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
A’s data link layer sends frame
R’s data link layer receives frame
R removes IP datagram from Ethernet frame, sees its destined to B
R uses ARP to get B’s physical layer address
R creates frame containing A-to-B IP datagram sends to B
A
R
B

## Slide 124
ARP operation

## Slide 125
ARP packet

## Slide 126
Encapsulation of ARP packet

## Slide 127
Example 1

## Slide 128: Layer 2 Devices

## Slide 129: Layer 2 Devices
NIC (Network Interface Card)
  Connect your computer with network.
  Provide MAC addresses to each connection.
  Implement CSMA/CD algorithm.
Bridge
  Forward or filter frame by MAC address.
Switch
  Multi-port bridge.

## Slide 130: NIC

## Slide 131: NIC (cont.)
Provides ports for network connection.
When selecting a network card, consider:
  Type of network:
    Ethernet
    Token Ring
    FDDI
  Type of media
    Twisted-pair
    Coaxial
    Fiber-optic
  Type of system bus
    PCI (Peripheral Component Interface)
    ISA

## Slide 132: NIC: Layer 2 functions
Logical link control (LLC): communicates with upper layers in the computer
Naming: provides a unique MAC address identifier
Framing: part of the encapsulation process, packaging the bits for transport
Media Access Control (MAC): provides structured access to shared access media
Signaling: creates signals and interface with the media

## Slide 133: Bridge
Connects network segments.
Make intelligent decisions about whether to pass signals on to the next segment.
Improve network performance by eliminating unnecessary traffic and minimizing the chances of collisions.
Divides traffic into segments and filters traffic based on MAC address.
Often pass frames b/w networks operating under different Layer 2 protocols.

## Slide 134: Bridge (cont.)

## Slide 135: Bridge (cont.): Filter

## Slide 136: Bridge (cont.): Forward

## Slide 137: Switch: Forwarding
How do determine onto which LAN segment to forward frame?
Looks like a routing problem...
hub
hub
hub
switch
1
2
3

## Slide 138: Self learning
A switch has a switch table
entry in switch table:
  (MAC Address, Interface, Time Stamp)
  stale entries in table dropped (TTL can be 60 min)
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table

## Slide 139: Filtering/Forwarding
When switch receives a frame:
index switch table using MAC dest address
if entry found for destination then{
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 140: Switch: traffic isolation
switch installation breaks subnet into LAN segments
switch filters packets:
  same-LAN-segment frames not usually forwarded onto other LAN segments
  segments become separate collision domains
hub
hub
hub
switch
collision domain
collision domain
collision domain

## Slide 141: Switches: dedicated access
Switch with many interfaces
Hosts have direct connection to switch
No collisions; full duplex
Switching: A-to-A’ and B-to-B’ simultaneously, no collisions
switch
A
A’
B
B’
C
C’

## Slide 142: Switching types
cut-through switching: frame forwarded from input to output port without first collecting entire frame
  slight reduction in latency
  Disadvantage?
Store-and-forward
combinations of shared/dedicated, 10/100/1000 Mbps interfaces

## Slide 143: LAN Switch: Micro-segmentation

## Slide 144: Institutional network
hub
hub
hub
switch
to external
network
router
IP subnet
mail server
web server

## Slide 145: Wireless Local Area Network (WLAN)

## Slide 146: IEEE 802.11 Wireless LAN
802.11b
  2.4-5 GHz unlicensed radio spectrum
  up to 11 Mbps
  direct sequence spread spectrum (DSSS) in physical layer
    all hosts use same chipping code
  widely deployed, using base stations
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
All use CSMA/CA for multiple access
All have base-station and ad-hoc network versions

## Slide 147: Base station approach
Wireless host communicates with a base station
  base station = access point (AP)
Basic Service Set (BSS) (a.k.a. “cell”) contains:
  wireless hosts
  access point (AP): base station
BSSs combined to form distribution system (DS)

## Slide 148: The 802.11 Protocol Stack
Part of the 802.11 protocol stack.

## Slide 149: IEEE 802.11 Standard

## Slide 150: Frequency Hopping Spread Spectrum (FHSS)
Band
    2.4 GHz ISM
Modulation & Data Rate
    FSK at 1 Mbaud/s
    1 or 2 bits/baud which results in a data rate of 1 or 2 Mbps.

## Slide 151: Direct Sequence Spread Spectrum (DSSS)
Band
    2.4 GHz ISM
Modulation & Data Rate
    PSK at 1 Mbaud/s
    1 or 2 bits/baud (BPSK or QPSK)

## Slide 152: Orthogonal Frequency Division Multiplexing (OFDM)—802.11a
Band
    5 GHz ISM
    52 subbands
Modulation & Data Rate
    PSK and QAM
    18 Mbps (PSK) and 54 Mbps (QAM)

## Slide 153: High-rate DSSS- 802.11b
Band
    2.4 GHz ISM
    Similar to DSSS except for the coding method
    Complementary Code Keying (CCK)
Modulation & Data Rate
    1, 2, 5.5 & 11 Mbps
    5.5 Mbps version uses BPSK and transmit 1.375 Mbaud/s with 4-bit CCK
    11 Mbps version uses QPSK and transmit at 1.375 with 8-bit CCK encoding.

## Slide 154: OFDM----802.11g
2.4 GHz

## Slide 155
Frame format

## Slide 156
Subfields in FC field
Field | Explanation
Version | The current version is 0.
Type | Type of information: management (00), control (01), or data (10).
Subtype | Defines the subtype of each type (see ).
To DS | Defined later.
From DS | Defined later.
More flag | When set to 1, means more fragments.
Retry | When set to 1, means retransmitted frame.
Pwr mgt | When set to 1, means station is in power management mode.
More data | When set to 1, means station has more data to send.
WEP | Wired equivalent privacy. When set to 1, means encryption implemented.
Rsvd | Reserved.

## Slide 157
Control frames

## Slide 158
Values of subfields in control frames
Subtype | Meaning
1011 | Request to send (RTS)
1100 | Clear to send (CTS)
1101 | Acknowledgment (ACK)

## Slide 159
Subfields in FC field
To DS | From DS | Address 1 | Address 2 | Address 3 | Address 4
0 | 0 | Destination station | Source station | BSS ID | N/A
0 | 1 | Destination station | Sending AP | Source station | N/A
1 | 0 | Receiving AP | Source station | Destination station | N/A
1 | 1 | Receiving AP | Sending AP | Destination station | Source station

## Slide 160
Addressing mechanism: case 1

## Slide 161
Addressing mechanism: case 2

## Slide 162
Addressing mechanism: case 3

## Slide 163
Addressing mechanism: case 4

## Slide 164
Bluetooth
Architecture
Radio Layer
Baseband Layer
Other Upper Layers
L2CAP Layer

## Slide 165
Piconet

## Slide 166
Scatternet

## Slide 167
Bluetooth layers

## Slide 168
Single-slave communication

## Slide 169
Multiple-slave communication

## Slide 170
Frame format types

## Slide 171
L2CAP data packet format